## Slide 1: Introduction Anders Plejdrup Houmøller CEO, Houmoller Consulting ApS
The concepts capacity, power and energy are explained in appendix 1
  Further, using the Nordic area and Western Denmark as cases, appendix 2 illustrates how the TSOs trade balancing energy and balancing capacity with market players
    In order to maintain the security of supply.
Appendix 3 contains a list of the terms and acronyms used in this presentation
This PowerPoint presentation is animated
  It’s strongly recommended to run the animation when viewing the presentation.
On most computers, you can start the animation by pressing F5.
  Now the presentation moves one step forward, when you press Page Down. It moves one step backward, when you press Page Up.

## Slide 2: The Single European Electricity Market
For The Single European Electricity Market,
this document has two messages:
In contrast: the electricity supply business will slide back
to planning economy, if the TSOs buy capacity on
medium-term or long-term contracts.
For the security of supply, with separation of
the TSOs’ markets for energy and capacity,
the green producers become part of the solution
Instead of being part of the problem
Please refer to slide no. 21.
1) The TSOs must establish separate markets for
balancing energy and balancing capacity
2) For capacity, the TSOs must establish short-term
capacity markets
  Thus providing a continuous updated price signal for capacity.
€

## Slide 3: Separation of the TSOs’ markets for capacity and energy
Referring to slide no. 10: the TSOs can ensure maximum competition at their market for balancing energy by separating their markets for energy and capacity.
Efficient competition at the TSOs’ market for balancing energy is vital for the competition at the retail market.
Because the prices for imbalances are derived from the TSOs’ prices for balancing energy.
A new retailer (with few customers) will have relatively high imbalances
  Buying the right amount of energy for every hour is difficult, when you have few customers
    As predicting a small customer portfolio’s consumption is relatively more difficult than predicting a big portfolio’s consumption.
  Thereby, at the retail market, high prices for imbalances create an high entrance barrier.
However, the TSOs can keep the imbalance prices in check by separating their markets for energy and capacity.

## Slide 4: Players at the TSOs’ capacity and energy markets
In order to promote innovation and competition, it’s very important the players are normal, commercial players
  Retailers, producers, traders, portfolio managers.
Every balance responsible player must be allowed to offer services at the TSOs’ capacity and energy markets.
As for the so-called ”smart grid” technologies:
  The investment in these technologies must be made solely by commercial players, who see a business opportunity
    An opportunity to use the technologies to offer more services at the TSOs’ markets for capacity and energy.
  The investments must not be made by the monopolies (ie, not by TSOs or distribution system operators).
We ensure the grid users will not end up paying for non-viable investments by ensuring smart grid investments are made by commercial players on fully commercial terms
  The TSOs’ job is solely to provide the price signal.
€

## Slide 5
Consumers
and producers
of electrical
energy, who
have the ability
to change
production/
consumption
Portfolio manager:
retailer or other
commercial player.
Aggregate small players’
service offers
Commercial
agreements
TSO. Buying
balancing capacity.
Buying and selling
balancing energy
balancing
energy: bids
and offers
balancing
capacity:
offers
Factories
Offices
House-
holds
District
heating
companies
Small power
producers

## Slide 6: Capacity markets in EU – 1
The electricity supply system gets more and more capacity from subsidized producers (eg, wind turbines and solar cells).
This drives down the market price of electrical energy as:
  Many of the subsidized producers receive feed-in tariffs. Hence they’ll produce without regard to the market price.
  For these producers: after their subsidy period has expired, they’ll still produce even if the market price is close to zero
    As their marginal production costs are close to zero.
Will this process drive non-subsidized producers out of business? (such as gas or coal fired power stations).
In order to maintain the security of supply, the TSOs need capacity
  Due to the process described above: in order to ensure sufficient capacity, will the TSOs have to buy capacity from otherwise non-subsidized producers on long-term or medium-term contracts?

## Slide 7: Capacity markets in EU – 2
Suppose the TSOs increased the purchase of capacity on medium-term or long-term contracts:
  Now no investor would build a new power station, unless it was subsidized.
Therefore, this would send us down the slippery slope
  Where no new power stations would be built, unless they were subsidized
    Subsidized due to environmental or security of supply issues.
Hence, a vital element of market economy would be lost for the electricity supply business
  In a market economy, one of the purposes of the price signal is to alert potential investors of scarcity of the commodity.
  With this element removed, the electricity supply business would slide back to planning economy.
The following slides will demonstrate how this can be avoided.

## Slide 8: The right type of capacity markets – 1
The TSOs can buy capacity on short-term contracts
  Buying capacity day-ahead, week-ahead and/or month-ahead.
Thereby, the TSOs do not pay for investments in power stations
  Instead, by means of their short-term capacity markets’ prices, the TSOs provide the market and potential investors with a price signal.
  This price signal will prompt investors to provide new capacity when it’s needed.
Hence, all we need is a short-term market for capacity providing a continuous updated price signal.
€

## Slide 9: The right type of capacity markets – 2
In order to create trust among potential investors, it’s imperative the framework for the TSOs’ markets for energy and capacity is regarded as stable and fair.
Building trust and reliable prices at a market is a very time-consuming process.
Hence, this work should start immediately
  And plans for medium-term or long-term capacity markets should be abandoned.
Otherwise, it will be unnecessarily expensive to meet EU’s goals for renewable energy.
Suppose the TSOs carry on buying capacity on medium-term or long-term contracts (perhaps even increasing this activity)
  In this case, for balancing capacity, the TSOs have signalled they do not believe it’s possible to create fair short-term markets with reliable prices
    This would be a costly surrender.
    And it would block the establishment of viable short-term capacity markets.

## Slide 10: Features of a well-designed short-term capacity market
As for the minimum amount of capacity players can offer at the TSOs’ capacity market:
  The allowed minimum must be very small
    As experience illustrates: this attracts capacity, which otherwise would not have been put to the market.
Players must be allowed to offer only up balancing capacity or only down balancing capacity (ie, asymmetric offers must be allowed)
  This makes it possible for unconventional players to offer capacity. For example:
  Smelteries and other types of industry (who can offer up regulation by temporary reducing consumption).
  District heating (who can offer down regulation by starting to produce hot water by means of electricity).
  Owners of a UPS (who can offer up balancing).
Note: precisely because it’s a short-term market, all these players (and many more) have the option of offering services at the TSOs’ markets (ie, enhancement of competition).

## Slide 11: Multinational markets needed! For energy and capacity
So far, the TSOs’ markets for balancing energy and balancing capacity have largely been national affairs.
If EU’s goals for renewables are to be met with reasonable costs, we need to improve this
  Enhance the competition by establishing a Single European Market for these services.
  Probably, due to grid bottleneck issues, the Single Market will work this way:
  For each bidding zone, the local TSO is the sole counterpart for the players
    ie, the players cannot themselves offer these services across the borders.
  However, the TSOs establish an EU-wide pricelist for the services – and trade with the ”best” counterparts
    To the extend grid bottlenecks do not prevent this.

## Slide 12: The common electricity market
What is actually common?
We have many markets.
Capacity markets
All operated by the TSOs
Primary reserves
Automatically, very
fast reacting units
Secondary reserves
Automatically, pretty
fast reacting units
Tertiary reserves
Activated manually
Energy markets
Balancing energy
Operated
by the TSOs
Day-ahead trading
Trading electrical
energy for tomorrow
Exchange plus
bilateral trading
Intra-day trading
Trading electrical
energy for today
Exchange plus
bilateral trading
Currently
mainly
national
markets
First made common
Some of them are:

## Slide 13
Appendix 1
concepts and units

## Slide 14: Concepts and units
Power
W
(Watt)
Energy
Wh
(Watt-hour)
During an hour:
how much water
was fed in, taken
out or flowing by?
Capacity
Concept
Unit
Water analogy
W
(Watt)
The ability to
change a flow
Flow: How much
energy per
second?
The amount
(for example,
during an hour)
Explanation
The ability to
change a flow
Flow: How much
water is being
fed in, taken out
or is flowing
by per second?

## Slide 15
Appendix 2
The TSOs’ markets for balancing energy and balancing capacity
The Nordic area and Western Denmark as cases
€

## Slide 16: The Nordic TSOs’ market for balancing energy
The producer has sold 200
MWh to the retailer. Price:
44 EUR/MWh
TSO
Sell 200 MWh to producer.
Producer’s purchase bid
price: 40 EUR/MWh
Result for TSO: a
production decrease
of 200 MWh
: buy at
40 EUR/MWh and sell
at 44 EUR/MWh
Producer’s marginal
costs are 41 EUR/MWh
Producer’s initial plan:
produce 200 MWh
R
Retailer
Producer
P
Example for an hour where the production is too big

## Slide 17: Offers and bids at the Nordic TSOs’ market for balancing energy – 1
All sellers in question
get this price
Sell reg. energy to TSOs
Price at spot
exchange
for this hour
(day-ahead
market price)
Example 1: during this
hour, the TSOs had
to buy this amount
of balancing energy
MWh
EUR/MWh
Buy reg. energy from TSOs
Example for one
Hour of Operation

## Slide 18: Offers and bids at the Nordic TSOs’ market for balancing energy – 2
Sell reg. energy to TSOs
Price at spot
exchange
for this hour
(day-ahead
market price)
All buyers in question
pay this price
Example 2: during this
hour, the TSOs had
to sell this amount
of balancing energy
MWh
EUR/MWh
Buy reg. energy from TSOs
Example for one
Hour of Operation

## Slide 19: Balancing energy – 1
The players at the Nordic TSOs’ market for balancing energy are paid the marginal price
  The last player’s price sets the price for everyone.

## Slide 20: Balancing energy – 2
Assume you are a player with both wind turbines
and gas fired power plants in your portfolio.
Probably, your forecast for the wind turbine production
will fail somewhat.
For the next Hour of Operation: assume your gas
fired power plants have spare capacity.
Should you keep the spare capacity as your own reserve?
This will enable you to adjust the production at the gas fired
power plants. Thus fluctuations in your wind turbine
production can be levelled out.
Thereby your total production will be according to plan.
Hence you’ll avoid settling an imbalance with the TSO.
Alternatively, you can use the spare capacity to send
balancing energy bids to the TSO.
Due to the marginal pricing of balancing energy: the most
profitable option is to use all your spare capacity to submit
bids to the TSO’s market for balancing energy.
Thereby, the marginal pricing automatically draws in the maximum
volume of bids to the TSOs’ market for balancing energy.
This is expedient for the security of supply.

## Slide 21: The Nordic market for balancing energy
At the latest 45 minutes before the start of the Hour of Operation,
players can send the local TSO the prices, at which they are willing
to buy and sell balancing energy.
Due to the separation of the TSOs’ markets for balancing energy
and balancing capacity, the TSOs ensure maximum participation
at the market for balancing energy:
  Players who could not offer capacity at the TSOs’ day-ahead
  markets for capacity, can offer to trade balancing energy
    For example: the owner of a wind farm, who knows the
    wind turbines will produce during the next Hour of
    Operation, can offer down regulating
      The owner will buy back energy at negative prices.
Thereby, for the security of supply, by separating the TSOs’
markets for energy and capacity – and by having a late deadline for
submitting bids to the TSOs’ energy market – the wind turbines
become part of the solution (instead of being part of the problem)
  With increasing amounts of intermittent energy sources,
  the TSOs’ markets for energy and capacity must be designed,
  so the green producers become part of the solution.

## Slide 22: Western Denmark (DK1) – 1
Consumption about 20 TWh/year.
Min. load about 1,200 MW. Max. load about 3,700 MW.
Wind turbines more than 4,200 MW (!).
In 2017, energy produced by wind turbines constituted more than 50% of the total Danish electricity production
  This is the world’s highest wind penetration.
  In Western Denmark it was 57%.
Still, with the world’s highest wind penetration, the DK1 security of supply was maintained solely by means of short-term capacity markets before the establishment of an electrical connection between Western and Eastern Denmark.

## Slide 23: Western Denmark (DK1) – 2
DK1 became a case of how the TSO’s purchase of capacity on a medium-term contract can play havoc with a short-term capacity market
  This happened after the establishment of an electrical connection between Western and Eastern Denmark.
The DK1 experience with short-term capacity markets illustrate two points:
  The short-term market’s price signal can attract lots of new capacity.
  TSO purchase of capacity on a medium-term contract can ruin a well-established short-term capacity market.

## Slide 24: Reserves bought by the TSO Western Denmark as a case
Primary reserve
(about 25 MW)
30 sec.
15 min.
Secondary reserve
(about 90 MW)
Order + 15 min.
Order
Tertiary reserve:
manually activated
reserve
MW
Time
FCR Frequency
Containment
Reserves
aFRR Frequency
Restoration
Reserves
Former name:
LFC automatic Load
Frequency Control
Day-ahead
purchase
Month-ahead
purchase
mFRR
Day-ahead
purchase
(in principle)

## Slide 25: Western Denmark – 3
The primary reserve is bought day-ahead. The capacity is autonomous
  “Self activating” when needed.
The supplier of the service must be able to maintain the regulation up to 15 minutes.
The secondary reserves are bought month-ahead. The capacity is activated automatically via an electronic signal from the TSO’s control room.

## Slide 26: Western Denmark – 4
The tertiary reserves were previously solely bought day-ahead
  Now, 300 MW have been bought via a medium-term contract.
  The day-ahead purchase is currently about 200 MW.
The tertiary reserves are activated manually.
Note: even if a player has not sold balancing capacity day-ahead, the player can send bids and offers to the TSO’s market for balancing energy
  The player’s capacity will be activated manually, if the TSO wants to trade with the player.
  Hence, a player’s capacity becomes part of the tertiary reserves, if the player sends bids to the TSO’s market for balancing energy shortly before the start of the next Hour of Operation
    At the latest 45 minutes before the start of the Hour of Operation.
    Due to the late enrolment, the player is not paid for putting the capacity at the TSOs’ disposal. There’s only settlement for energy (if the player’s capacity is activated).
For balancing energy from the manually activated units, there is a common Nordic market.
All the information on the slides no. 16 – 21 refers to balancing energy delivered from manually activated units.

## Slide 27
Appendix 3
Terminology and acronyms

## Slide 28: Terminology and acronyms – 1 As used in this presentation
Balancing capacity Capacity the TSOs buy in order to ensure the security of supply.
The TSOs’ purchase of capacity ensures, the TSOs will always have balancing energy available.
By changing the energy production/consumption of the capacity bought by the TSOs, the TSOs can ensure a balance between total production and total consumption.
Balancing energy Energy which the TSOs buy or sell in order to maintain the security of supply (ie, maintain a balance between the total consumption and the total production). The TSOs’ counterparties are commercial market players.
Balance responsible player A player who is responsible for settling imbalances with the TSO.
For a retailer, an imbalance occurs if the customers’ hourly consumption does not fit the retailer’s hourly purchase.
For a producer, an imbalance occurs if the producer’s production does not fit the producer’s sale.
A balance responsible player may also be portfolio manager, who settles imbalances on behalf of other market players.

## Slide 29: Terminology and acronyms – 2 As used in this presentation
Bidding zone A geographical area, within which the players can trade electrical energy day-ahead without considering grid bottlenecks.
Day of Operation The day where the electrical energy is produced and consumed.
DK1 Western Denmark.
Down regulating A player buying electrical energy from the TSO.
It’s either a producer reducing the production or a consumer increasing the consumption.
EU European Union.

## Slide 30: Terminology and acronyms – 3 As used in this presentation
Hour of Operation The hour where the electrical energy is produced and consumed.
Long-term purchase of capacity Purchase where the capacity bought by the TSO must be put at the TSO’s disposal for more than five years.
It’s implied the capacity is bought shortly before entering the period where the TSO has disposal of the capacity.
Medium-term purchase of capacity Purchase where the capacity bought by the TSO must be put at the TSO’s disposal for more than one month and up to five years.
It’s implied the capacity is bought shortly before entering the period where the TSO has disposal of the capacity.
Nordic and Nordic area refer to the countries Denmark, Finland, Norway and Sweden.

## Slide 31: Terminology and acronyms – 4 As used in this presentation
Short-term purchase of capacity Purchase where the capacity bought by the TSO must be put at the TSO’s disposal for maximum one month.
It’s implied the capacity is bought shortly before entering the period where the TSO has disposal of the capacity.
In practice, this is capacity bought day-ahead, week-ahead or month-ahead.
UPS Uninterruptible Power Supply. An electrical apparatus that provides emergency power when the main power fails.
For example, a hospital normally have an UPS.
TSO Transmission System Operator. An organisation owning and operating the transmission grid in a given area, and responsible for this area’s security of supply.
Up regulating A player selling electrical energy to the TSO.
It’s either a producer increasing the production or a consumer reducing the consumption.

## Slide 32: Thank you for your attention!
Anders Plejdrup Houmøller
Houmoller Consulting ApS
Tel. +45 28 11 23 00
anders@houmollerconsulting.dk
Web houmollerconsulting.dk