## Slide 1: Introduction
For the European Union’s electricity market, this presentation discusses the calculation of spot prices and market coupling flows.
In the appendix, you’ll find a list of the terms and acronyms used in this presentation.
Concerning the documents referred to in this presentation:
  Unless otherwise mentioned, you can download the documents from http://www.houmollerconsulting.dk/facts-findings/.
This PowerPoint presentation is animated
  It’s recommended to run the animation when viewing the presentation.
On most computers, you can start the animation by pressing F5.
  Now the presentation moves one step forward, when you press Page Down. It moves one step backward, when you press Page Up.

## Slide 2: Flow-based market coupling – 1
Flow-based market coupling considers the spatial interdependency of the power supply system
  The allowed production surplus/deficit in one bidding zone is dependent on the production surpluses/deficits in all the other bidding zones.
The so-called PTDF matrix describes a simplified, linear version of this spatial interdependency
  PTDF Power Transfer Distribution Factor.

## Slide 3: Flow-based market coupling – 2
The idea is to have a simplified,
linear grid model included in the
calculation of tomorrow’s spot prices
and market coupling flows.
  Thereby, the software can see,
  how big production surpluses/
  deficits we can have per bidding
  zone without overloading any
  interconnector.
    Also, the software can ensure,
    we run according to the
    ”n-1 criterion”
”Linear” means you have a
starting point P0 for tomorrow’s flows
and production surpluses/deficits.
Next, you assume deviations
from P0 gives a linear response.
P0:
1000 MW
production
surplus
      ie, the system can cope will the unplanned outage of
      one big production unit or one important power line.

## Slide 4: Spot calculation – 1
Every day, shortly after noon Central European Time, the spot software calculates the spot prices and the market coupling flows for the coupled area.
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
All bidding zones and all interconnectors in the
coupled region are included in the calculation.

## Slide 5: Spot calculation – 2 The effect of block bids
Hour no. 3
Hour no. 2
…
Hour no. 1
Hour no. 24
The block bids create a time inter-dependence between
the 24 hours of the next day.
You cannot calculate the prices and the flows for one hour only.
And it does not make sense to optimize
the solution for one hour only.
In one go, you must calculate spot prices and
market coupling flows for all bidding zones,
all interconnectors and all 24 hours
of the next day
The algorithm must search for
an optimal solution for
all 24 hours of the next
day and for the whole
coupled area.

## Slide 6: The optimal solution – 1
Even if we do not use flow-based market coupling:
  Due to the block bids, the optimal solution will normally have hours where an interconnector is not fully utilized, although it connects two bidding zones with different spot prices.
High spot
price
Low spot
price
Uncongested

## Slide 7: The optimal solution – 2
High spot
price
Low spot
price
This illustrates that it does
not make sense to ask
if the solution is optimal
during one hour and/or for
one interconnector only.
…
The truly optimal solution in a
meshed grid defies intuition
Strange!
As this solution will often have
flows towards the low price
for some interconnectors
In order to ship as much energy as
possible to some high-price zones.
Because flow-based market coupling
aims at this truly optimal solution:
The best flow-based solution will
often have such counter-intuitive flows.
For more information on the optimal
solution, see the PowerPoint
presentation “Welfare criterion”.

## Slide 8
Appendix
Terminology and acronyms

## Slide 9: Terminology and acronyms – 1
Bidding zone A geographical area, within which the players can trade electricity day-ahead without considering grid bottlenecks.
Block bids Please refer to the PowerPoint presentation “Market coupling – European price coupling”.
Border A border between two bidding zones. Hence, it need not be a border between two countries. It may be a border between two bidding zones in the same country.
Coupled area For EU, you’ll find a map of the coupled area at https://www.entsoe.eu/network_codes/cacm/implementation/sdac/
However, market coupling and spot trading is also used in India, for example. See https://www.iexindia.com/.
Interconnector In this document, this is a power line connecting two bidding zones.
Market coupling A day-ahead congestion management system, where the plans for tomorrow’s cross-border energy flows are calculated using:
The purchase bids and sales offers sent by market players to spot exchanges.
The day-ahead cross-border trading capacity for each interconnector.
For more information, see the PowerPoint presentation “Maximizing the economic value of market coupling and spot trading”. You may also refer to the PDF document “The Liberalized Electricity Market”.

## Slide 10: Terminology and acronyms – 2
Spot calculation The simultaneous calculation of tomorrow’s spot prices and market coupling flows.
For more information, see the PowerPoint presentation “Maximizing the economic value of market coupling and spot trading”. You may also refer to the PDF document “The Liberalized Electricity Market”.
Spot exchange See the PowerPoint presentation “Maximizing the economic value of market coupling and spot trading”. You may also refer to the PDF document “The Liberalized Electricity Market”.
Spot price See the PowerPoint presentation “Maximizing the economic value of market coupling and spot trading”. You may also refer to the PDF document “The Liberalized Electricity Market”.
Spot software The software performing the spot calculation. In EU, the algorithm used is called Euphemia.
€
€

## Slide 11: Thank you for your attention!
Anders Plejdrup Houmøller
Houmoller Consulting ApS
Tel. +45 28 11 23 00
anders@houmollerconsulting.dk
Web houmollerconsulting.dk