## Slide 1: Introduction
In the appendix, you’ll find a list of the terms and acronyms used in this PowerPoint presentation.
This PowerPoint presentation is animated
  It’s strongly recommended to run the animation when viewing the presentation.
On most computers, you can start the animation by pressing F5.
  Now the presentation moves one step forward, when you press Page Down. It moves one step backward, when you press Page Up.

## Slide 2: Welfare criterion
This PowerPoint presentation explains the so-called “welfare criterion”.
Actually, the name is misleading, as the criterion does not aim at maximising society’s welfare.
More modest, the criterion aims at maximising the economic value of the spot trading.
Referring to the figure on the next slide:
  On slide no. 14 it’s explained in detail why the area between the supply curve and the demand curve is the traders’ total surplus.

## Slide 3: Traders’ surplus: no import/export
For one hour for one price zone: The buyers’ and the sellers’ total surplus from the spot trading is the area between the spot exchange’s supply curve and the spot exchange’s demand curve (the red/green area A).
Buyers’ surplus
(red area)
EUR/MWh
MWh
Sellers’ surplus
(green area)
Supply curve
Spot price
Area A: The sum of the
red and the green areas
Demand curve

## Slide 4: Traders’ surplus if the zone is exporting
For one hour for an exporting price zone:
The difference between the local purchase from the exchange and the local sale to the exchange is the energy exported by the implicit auction system (this energy needs to be exported, as it is sold to the exchange; but not bought locally).
The export drives up the local price. Furthermore:
A. The increase in spot price redistributes some of the local surplus to sellers
from buyers.
B. There is an increase in the total surplus. This is allocated to the sellers.
Extra surplus from expor-
ting (allocated to sellers)
Bought from exchange
Sold to exchange
MWh
EUR/MWh
Supply curve
}
Export
Price with export
Price without export
Surplus redistri-
buted to sellers
from buyers
Demand curve

## Slide 5: Traders’ surplus if the zone is importing
For one hour for an importing price zone:
The difference between the local purchase from the exchange and the local sale to the exchange is the energy imported by the implicit auction system (this energy needs to be imported, as it is bought from the exchange; but not sold locally).
The import drives down the local price. Furthermore:
A. The decrease in spot price redistributes some of the local surplus to buyers
from sellers.
B. There is an increase in the total surplus. This is allocated to the buyers.
Extra surplus from impor-
ting (allocated to buyers)
Price without import
Surplus redistri-
buted to buyers
from sellers
}
Import
Sold to exchange
Bought from exchange
MWh
EUR/MWh
Price with import
Demand curve
Supply curve

## Slide 6: Value created by the trading
For one hour of the next day: consider two neighbouring price zones with different prices Plow and Phigh.
If the implicit auction sends the energy E from the low-price zone to the high-price zone, the so-called congestion revenue (or congestion rent) is
  E * (Phigh – Plow).
Normally, the congestion rent is given to the capacity owners.
Actually, the total value created by the spot trading is the sum of the following two components:
  The sum of all the red/green areas (the traders’ surplus).
  The congestion rent (the capacity owners’ gain).

## Slide 7: Optimization – 1
When selecting the preferred solution, the spot trading software aims at maximising the value of the spot trading.
With reference to the previous slides: it aims at maximising the sum of
  The traders’ surplus (all the red/green areas).
  The congestion rent.
The maximization runs over all links, all price zones and all 24 hours of the next day.
Hence, the software aims at maximising the following sum:
Σ [ Σ (congestion rent) + Σ (traders’ surplus)]
24 hours
All links
between
price zones
All
price
zones

## Slide 8: Congestion revenue and traders’ surplus for one hour. Only two price zones
Price Plow
Red areas: buyers’ surplus
Green areas: sellers’ surplus
Exporting zone
EUR/MWh
MWh
Exported
energy E
}
Importing zone
EUR/MWh
MWh
Price Phigh
}
Imported
energy E
Congestion revenue:
E * (Phigh – Plow)
}
E

## Slide 9: Buyers’ utility and sellers’ cost
The buyers’ utility is the area under the exchange’s demand curve
(yellow area: from the second axis to the purchase volume)
The sellers’ cost is the difference between the two blue areas:
(blue area over the first axis) - (blue area under the first axis)
Buyers’
utility
Buyers’
utility
If the zone is exporting
If the zone is importing
Price with
export
Price with
import
}
Export
Sellers’
cost
}
Import
Sellers’
cost

## Slide 10: Optimization – 2
Σ [ Σ (congestion rent) + Σ (traders’ surplus)]
24 hours
All links
between
price zones
All
price
zones
Σ Σ [(buyers’ utility) – (sellers’ cost)] =
24 hours
All
price
zones
You can prove the following equality:
Therefore, the ”welfare criterion” also aims at maximising the
difference between the buyers’ utility and the sellers’ cost.
Which precisely means maximising
the value of the spot trading.
*) For the mathematically
interested, Houmoller Consulting
has a paper proving the equality.
*)
**) Slide no. 9 illustrates the equation’s
left-hand side. Slide no. 8 illustrates
the equation’s right-hand side.
**)

## Slide 11: Notes
The absolute value of the red/green areas should not be considered important
  As it’s heavily dependent upon the spot exchange’s choice of maximum price and minimum price.
However, when comparing different solutions, the relative size of the areas can be used to select the best solution.
When this is used to select the preferred solution, the value of the spot trading is maximised
  The bilateral trading and the exchange intra-day trading is invisible for the spot trading software. Therefore this cannot be included in the optimization.
Max. price
Min. price
Max. price
Min. price

## Slide 12: Appendix – terminology and acronyms – 1 As used in this presentation
Double auction A calculation method whereby an exchange’s price is set by calculating the intersection between the exchange’s supply curve and the exchange’s demand curve.
Implicit auction The common term for market coupling and market splitting.
Market coupling A day-ahead congestion management system, you can have on a border, where two electricity exchanges meet. The day-ahead plans for the cross-border energy flows are calculated using the two exchanges’ bids and information on the day-ahead cross-border trading capacity.
Market splitting A day-ahead congestion management system, you can have on a border, where you have the same electricity exchange on both sides of the border. The day-ahead plans for the cross-border energy flows are calculated using the exchange’s bids and information on the day-ahead cross-border trading capacity.

## Slide 13: Appendix – terminology and acronyms – 2 As used in this presentation
Price zone A geographical area, within which the players can trade electrical energy day-ahead without considering grid bottlenecks.
Spot bid A purchase bid or a sales offer submitted to a spot exchange.
Spot exchange In this document, a spot exchange is an exchange where
  Electrical energy is traded day-ahead.
  The exchange’s day-ahead prices are calculated by means of double auction.
Spot price A price calculated by a spot exchange. Either by a calculation performed by the spot exchange itself, or by a calculation performed by a body, to which the calculation has been outsourced.
Spot trading software The software calculating the spot prices and the day-ahead plans for the cross-border energy flows.

## Slide 14: Welfare criterion explained in detail No exchange of energy with other price zones
Please refer to the figure above. Here, we consider the buyers’ and the sellers’ surplus for one MWh.
The buyers are willing to pay a rather high price for this MWh. However, also for this MWh, the buyers will pay the spot price.
Hence the buyers’ surplus for this MWh is the red area:
[(The buyers’ bid price for this MWh) – (The spot price)] * 1 MWh
For the MWh in question, the sellers are willing to sell at a rather low price. However, also for this MWh, the sellers will get the spot price.
Hence the sellers’ surplus for this MWh is the green area:
[(The spot price) – (The sellers’ offer price for this MWh)] * 1 MWh
Now please refer to the picture on slide no. 3 in this PowerPoint presentation: by considering all the energy traded, we conclude from the argument above that the total surplus for both the sellers and the buyers is the area between the supply curve and the demand curve.
Demand
Supply
Spot price
Buyers are willing to
pay this price for this MWh
Buyers’ surplus for this MWh: The difference
between the spot price and the bid price
Sellers’ surplus for this MWh: The difference
between the offer price and the spot price
MWh
EUR/MWh
Sellers are willing to sell
this MWh at this price
}
1 MWh

## Slide 15: Thank you for your attention!
Anders Plejdrup Houmøller
Houmoller Consulting ApS
Tel. +45 28 11 23 00
anders@houmollerconsulting.dk
Web houmollerconsulting.dk