## Slide 1: Introduction Anders Plejdrup Houmøller, CEO Houmoller Consulting ApS
Appendix 1 defines what intra-day trading of electricity means in a large part of Europe.
Appendix 2 contains a map of 5 of the synchronous grids in Europe – and a map showing the seven DC links between UCTE and Nordel.
Appendix 3 contains a list of the terms and acronyms used in this presentation.
Concerning documents referred to in this presentation:
  At houmollerconsulting.dk, you can download the documents from the sub-page Facts and findings.
This PowerPoint presentation is animated
  It’s strongly recommended to run the animation when viewing the presentation.
On most computers, you can start the animation by pressing F5.
  Now the presentation moves one step forward, when you press Page Down. It moves one step backward, when you press Page Up.

## Slide 2: European intra-day trading
A capacity database is needed for the future pan-European intra-day trading.
The database will inform traders and trading platforms on the intra-day capacity between the price zones
  For example: the database will inform whether it’s possible to trade 10 MWh from Northern Sweden to France.
The establishment and operation of the database is a monopoly task
  Just as grid building and grid operation are monopoly tasks.
However, usage of the database for trading is a commercial task
  Just as the market players’ usage of the grid is commercial.
Therefore, we need a separation of the monopoly and the commercial tasks
  Similar to the separation we have for the grid.

## Slide 3: Separating monopoly tasks and commercial tasks
Commercial
activity:
bilateral
intra-day
trading
Intra-day
trading
platform 1
Intra-day
trading
platform N
Commercial
activity:
intra-day
trading via
a platform
Capacity
database
The TSOs must establish and operate the capacity database.
This is the monopoly task.
Blue and red colours indicate commercial tasks.
Commercial
service
providers

## Slide 4: The capacity database
Inside a synchronous area, you cannot control the flow of energy
  Therefore, the database cannot choose the routes for the energy flows created by an intra-day trade
    The AC laws of nature will decide how the energy flows from source to sink.
  When setting the capacity between two price zones inside a synchronous area, the database must make a (preferably flow-based) estimate
    ”Flow-based” means the estimate takes into account the complicated flow patterns of a meshed AC grid.
However, for a DC link the TSOs can set the link’s flow to a given value
  Hence, for trades between two asynchronous areas the database must choose which DC link(s) to use.

## Slide 5: An intra-day trading case The function of the capacity database
Consider a 10 MWh trade from Northern Sweden (SE1) to France.
  This is a trade between two asynchronous areas: Nordel and UCTE (please refer to slide no. 15).
There are seven DC links between Nordel and UCTE.
Assume there’s 10 MW capacity available on all the seven DC links. In this case: which links should be used for the trade?
There are 127 different ways of combining the seven links – for example:
  Use NorNed, Kontek and Greater Belt.
  Use Skagarrak and Swepol.
  Etc.
For each of the 127 combinations, the database must decide how much energy to ship along each of the selected links
  Hence, there’s an infinite number of ways to use the selected combination, even after having selected one of the 127 combinations of links…

## Slide 6: The function of the capacity database
For a trade from Northern Sweden (SE1) to France: for each potential usage of the DC links, the database must determine
  Whether the Nordel grid can cope with the internal Nordel flows generated by this specific usage of the DC links.
  Whether the UCTE grid can cope with the internal UCTE flows generated by this specific usage of the DC links.
These kinds of investigations will set the intra-day capacities between all price zones
  Naturally, the investigations are made in advance
    Before the players start intra-day trading.
    Also, after each intra-day trade, an update must be made.
For trades between two asynchronous grids, the database will often have a choice of how to use the DC links.
The database’s choice will determine which trades can be carried out subsequently
  Example for a trade from SE1 to France: the trade will consume capacity at the Polish-German border, if SwePol is used.

## Slide 7: The capacity database has two functions
Capacity database
and DC flow selection
Function 1
Inform on the
capacities between
price zones
Function 2
For trades between
asynchronous grids:
choose how to use
the DC links
Concerning function 2: the IT system
needs a criterion when selecting among
the many possible ways of using DC
links connecting asynchronous grids.
Choosing the criterion is part of the monopoly task.
  And it must be done in a transparent way.
  Public consultation etc.
Actually, it’s a database and a DC flow selection module

## Slide 8: The monopoly task and the commercial tasks
Establishing the database is the complicated part.
Setting up trading platforms using the database is relatively trivial.
As the database grants access for bilateral trading and multiple trading platforms:
  Competition will keep the trading platform fees in check.
Regulators must set/approve the fees for using the database, as this is a monopoly.

## Slide 9: Pan-European governance
Spot Market Council
User representation
Board
National representation
Capacity database
and DC flow selection
ACER and national regulators
If there turns out to be a single, monopoly intra-day
trading platform, this is the governance for both the
trading platform and the database/DC flow selection

## Slide 10
Unbundling

## Slide 11: Unbundling – 1
Unfortunately, the spot exchanges become monopolies when market coupling or market splitting is introduced as the day-ahead congestion management system
  Please refer to the PowerPoint presentation Market coupling makes real competition betw. spot exchanges unfeasible.
Hence, in order to avoid cross-subsiding, the spot exchanges must unbundle
  Unbundling means an organisation having a monopoly task cannot have any other business
    Hence, cross-subsidising is automatically prevented
      The regulators can focus on controlling the organisation’s economical efficiency
        Please refer to the PDF document Unbundling of spot exchanges and associated clearing houses.

## Slide 12: Unbundling – 2 Terminating cross-subsidizing
Note: this also means the spot exchanges cannot be involved in intra-day trading
  As experience shows: this gives heavy cross-subsiding – with the many spot players subsidizing the fewer intra-day players.
As cases – turn-over for the year 2013 (numbers in TWh):
  EPEX Spot (Austria, France, Germany, Switzerland)
    Spot turnover 323
    Intra-day turnover 23
  Nord Pool Spot
    Spot turnover (Baltic-Nordic area) 349
    Intra-day turnover (Baltic-Nordic, Germany) 4
  APX (Belgium, the Netherlands)
    Spot turnover 64
    Intra-day turnover 1
  As can be seen: the turnover at the intra-day markets is paltry. It cannot finance the intra-day trading platforms
    Hence the intra-day trading platforms only survive due to heavy cross-subsidizing from the spot trading.

## Slide 13: Unbundling – 3
Terminating the spot market players
subsidizing the intra-day trading platforms
Adding insult to injury: as a
consequence of the
cross-subsidizing, small
market players are
subsidizing big players
First and foremost, the intra-day
market is important for big players
Who face the risk of big, unplanned outages.

## Slide 14: Appendix 1 Time line for trading electrical energy in a large part of Europe
Time
Day of operation (D)
Midnight
Midnight
Day of operation:
The day where the electrical energy is produced and consumed.
Hour of operation:
The hour where the electrical energy is produced and consumed.
Long-term trading
Day-ahead trading
Intra-day trading
Trading regulating
energy with TSO
D - 1
Midnight
hour of
operation
12 o’clock CET:
gate closure
time for spot
trading

## Slide 15: Appendix 2 Five of the synchronous grids in Europe
SE1
RG Continental Europe (UCTE)
RG Baltic
RG United Kingdom
RG Ireland
RG Nordic (Nordel)

## Slide 16: Appendix 2 The 7 DC links between Nordel and UCTE
NorNed Norway–the Netherlands
NorNed
Skagerrak Norway–DK1
Skagerrak
Konti-Skan Sweden–DK1
Konti-
Skan
Great Belt DK2–DK1
Great Belt
Baltic Cable Sweden–Germany
Baltic
Cable
SwePol Sweden–Poland
SwePol
Kontek
Kontek DK2–Germany
DK1: Western Denmark DK2: Eastern Denmark

## Slide 17
Appendix 3
Terminology and acronyms

## Slide 18: Terminology and acronyms – 1
AC Alternating current.
CET Central European Time.
DC Direct current.
EPEX Spot See the web page epexspot.com.
Nord Pool Spot See the web page nordpoolspot.com.
Price zone A geographical area, within which the players can trade electrical energy without considering grid bottlenecks.
SE1 Sweden’s northernmost price zone. Please refer to slide no. 15.
Synchronous grid An electricity grid that operates at a synchronized frequency and is electrically tied together during normal system conditions.
In popular terms: in a synchronous grid, the electrons oscillate in lockstep.
Two asynchronous grids can only be connected by means of DC links.

## Slide 19: Terminology and acronyms – 2 As used in this presentation
Trading platform A computer system that can be used to place sales offers and purchase bids for electrical energy. The platform can also be used to execute trades.
The platform is similar to the electronic trading platforms used for trading shares, bonds and currencies.
If a trading platform has access to a capacity database, the platform may include cross-border trading.
Currently, each of the exchanges EPEX Spot and Nord Pool Spot operate a trading platform (Elbas is Nord Pool Spot’s platform). However, neither of these platforms carry out pan-European intra-day trading. Also, these platforms are operated by exchanges engaged in spot trading
  Hence there’s a lack of unbundling, as market coupling has made these spot exchanges monopolies. Please refer to the PowerPoint presentations Market coupling – transparency, type, quality and unbundling and Market coupling makes real competition betw spot exchanges unfeasible.
TSO Transmission System Operator.

## Slide 20: Thank you for your attention!
Anders Plejdrup Houmøller
Houmoller Consulting ApS
Tel. +45 28 11 23 00
anders@houmollerconsulting.dk
aph@copenhageneconomics.com
Web houmollerconsulting.dk